Jansen Doors

Fire Protection – Telescopic sliding door ORPHEUS

OPTIONAL: 1 leaf or 2 leaves

Leaf panels: OPTIONAL 1 or 2 panels

Classified performance: 
EI2 30 C
Fire retardant and self-closing

Additional performance:
Durability of self-closure: C2 (10,000 load cycles)

Tightly closing = Sa

Equipment:

Door sections individually suspended on ball bearing runners

Door leaf and running rails made of galvanized sheet metal

The running rails can be fixed to the wall or ceiling using brackets

Floor guide outside the clear opening

Self-closing via weights with radial dampers

Damping by rubber buffers

With bow-type handle and wall-side shell-type handle

Dimensions :

Clear door height :

Clear door width :

Lintel height :

Controls:

Hold-open system with smoke switches, number according to DIBt guidelines

Power supply unit including release button

1 x signal transmitter as combination optical/acoustic

Installation method for electrical components: Plastic cable duct, light grey

Reference product

Jansentore GmbH & Co. KG  -  Telescopic sliding door ORPHEUS

www.jansentore.com