Jansen Doors

Fire Protection – Stacking door HERO

Classified performance: 
EI2 30 C
Fire retardant and self-closing

Additional performance:
Durability of self-closure: C2 (10,000 load cycles)

Tightly closing = Sa

Door leaf: 
Door sections with ball-bearing rollers, when open stacked behind the lintel to save space.

Safety chain incl. fall protection according to DIN EN 12604

Door leaf and running rails made of galvanized sheet steel

Minimum lintel height 740 mm

Dimensions :

Clear door height :

Clear door width :

Lintel height :

Control & Drive:

Fire protection drive 400V/16A with centrifugal regulator for a controlled closing speed.

(Builder-owner provided: 400 V/16A supply cable with CEE plug near the door)

Dimensions control box (WxHxD): 400 x 500 x 210 mm

VdS-tested, battery-buffered for approx. 4 hours, hold-open system with smoke switches, number according to DIBt guidelines.

Release button: 1x single button red rocker

1 x signal transmitter as combination optical/acoustic

Floor closure with self-monitoring safety strip.

Locking function and closing also in case of power failure.

Operation with a double surface-mounted push-button.

Mode of operation: Dead man

Installation method for electrical components: Plastic cable duct light grey

Reference product

Jansentore GmbH & Co. KG  -  Stacking door HERO

www.jansentore.com