ATEX-sectional door

- Premium ATEX-sectional doors according to 94/9/EG and 1999/92/EG for hazardous areas.

- Available for zone 1/2 and 21/22.

- Combinable with requirements for sound insulation.

Door leaf:

The door leaf is made of 460 mm high, stucco aluminium-panels with horizontal corrugations. The thickness of the PU-foamed sections is 40 mm. The door leaf is also possible with aluminium-bar-construction in a glazed or closed design. Execution as lifting door possible.

Surface:

The aluminium-frame-sections are E6/ EV1 anodized.

Guide rail:

The vertical guide rails (galvanized steel) come with an outer profile seal up to the lintel.

Fitting:

Standard fittings for a lintel height of 380 mm, depending on the size of the door. Further types of fittings such as high lift fittings, fittings for slanted roofs, low headroom or vertical fittings are possible.

Operation:

Manually via hand chain or an explosion-prevented electric drive. Individually adjusted springs above the lintel ensure a balanced running of the door.

For large doors or doors with frequent cycles an electric drive without spring compensation is advisable. This advantageous drive technology is very maintenance-friendly and ensures a long lifespan.

Placement of drive and control inside or outside the ATEX-zone, depending on requirements.

Supplementary equipment:

- Surface coating: colouring according to RAL, DB or NCS

- Safety features: light barrier, switch rail explosion-prevented

- Impulse transmitter: push button "Open-Stop-Close", pull switch, key switch explosion-prevented

- Intrinsically safe light barrier

- Mechanical interlock

- Postern door integrated into door leaf

- Side door in the same design of the door leaf